## Slide 1
Date: 2023/05/22
APRS Reference PDR
FERRER, Javier

## Slide 2: Function and Performance
Purpose : Provide satellite APRS Digipeating service for Amateur Radio Community.
Function 1: Digipeater APRS packets from amateur radio stations on the ground.​
Performance 1a: Transmit satellite APRS beacon to ground​
Performance 1b: Receive and retransmit APRS packets from amateur radio stations.
Performance 1c: Transfer the received data packets to desired micro controller.

## Slide 3: Function and Performance
Function 2 : Store the received data.​
Performance 2a: Store the data to satellite’s specified memory location.​
Function 3 : Data transfer to the COM MCU​.
Performance 3a: Transfer stored data to COM MCU for download via UHF 4800 bps to ground stations.

## Slide 4: Block Diagram

## Slide 5: Block Diagram

## Slide 6: System Main Components
Transceivers:
Radiometrix BiM1H
(BIRDS Heritage)
Nice RF SA818V
(PSAT-2 satellite aka NO-104)
Terminal Node Controller
ATMEGA 1284P
(from Byonics TT4)

## Slide 7: Schematics

## Slide 8: Schematics

## Slide 9: PCB design

## Slide 10: APRS-DP test setup
BIRDS-3
FAB
MCX to SMA Cable
+5V lines
SDR+Computer
UART to USB cable
SDR + Computer
APRS capable radio
Antenna

## Slide 11: APRS-DP test results
TNC Lights
Beacon from APRS board
APRS message from handheld radio
APRS message relay from APRS board
Confirmation message relay from APRS board to handheld radio
BIRDS-3
FAB
MCX to SMA Cable
LED turn on

## Slide 12: APRS tests results
TNC Lights
BIRDS-3
FAB
MCX to SMA Cable

## Slide 13: APRS tests results
TNC Lights
BIRDS-3
FAB
MCX to SMA Cable

## Slide 14: RAS: APRS-R
SR1.1 - Payload shall be controllable through an uplink command from a control ground station |  |  |  |  | 
ID | Design Requirements | ID | Verification Requirements | Verification Method | Status
DR1.1.1 | Command will be sent from ground station using UHF uplink frrequency | VR1.1.1.1 | Measure receivable signal power of COMM transceiver | Using spectrum analyzer | Δ
DR1.1.2 | OBC will relay the command to Mission Boss to activate APRS Reference payload | VR1.1.2.1 | Check if the APRS/SF-WARD payload is activated/deactivated | Using terminal software to read APRS reference MCU | ○
Reference: | ○ | Successful / Verified
 | Δ | Partially successful / More tests required
 | × | Failed / Not tested yet

## Slide 15: RAS: APRS-R
SR1.2 - VHF transceiver operating in half-duplex will receive data from amateur radio users/ground terminal |  |  |  |  | 
ID | Design Requirements | ID | Verification Requirements | Verification Method | Status
DR1.2.1 | Receiver will demodulate FM signal received | VR1.2.1.1 | Check AFSK output of receiver | Using spectrum analyzer | Δ
DR1.2.2 | TNC will decode received AFSK signal | VR1.2.2.1 | Check data output of TNC | Display serial output of TNC through serial monitor on PC | ○
DR1.2.3 | APRS reference payload will receive transmitted data and store it | VR1.2.3.1 | Check received data if it matches transmitted data through wired testing | Display received OBC data through serial on PC | ○
 |  | VR1.2.3.2 | Check stored data in flash memory | Read flash memory through APRS reference serial interface | ○
Reference: | ○ | Successful / Verified
 | Δ | Partially successful / More tests required
 | × | Failed / Not tested yet

## Slide 16: RAS: APRS-R
SR1.3 - Payload shall store received packets (APRS message and ground sensor) into memory |  |  |  |  | 
ID | Design Requirements | ID | Verification Requirements | Verification Method | Status
DR1.3.1 | APRS reference MCU shall process received AX.25 frame into the correct fields | VR1.3.1.1 | Check processed data of APRS reference MCU | Display processed data through serial interfase | ○
DR1.3.2 | Flash memory of capacity of at least 32 MB | VR1.3.2.1 | Check specification and writable memory | Through write operations | Δ
Reference: | ○ | Successful / Verified
 | Δ | Partially successful / More tests required
 | × | Failed / Not tested yet

## Slide 17: RAS: APRS-R
SR1.4 - Payload shall transmit stored data to ground station upon command from ground station using COM data downlink frequency |  |  |  |  | 
ID | Design Requirements | ID | Verification Requirements | Verification Method | Status
DR1.4.1 | COMM MCU shall read stored memory in APRS reference flash memory for downlink | VR1.4.1.1 | Check data transmitted by COMM | Display received data | Δ
Reference: | ○ | Successful / Verified
 | Δ | Partially successful / More tests required
 | × | Failed / Not tested yet

## Slide 18: Schedule
TNC Lights
BIRDS-3
FAB
MCX to SMA Cable
 | TASK | 2022 |  |  |  |  | 2023 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | DEC |  |  |  |  | JANUARY |  |  |  |  | FEBRUARY |  |  |  | MARCH |  |  |  | APRIL |  |  |  | MAY |  |  |  |  | JUNE |  |  |  | JULY |  |  |  | AUGUST |  |  |  |  | SEPTEMBER |  |  |  | OCTOBER |  |  |  | NOVEMBER |  |  |  |  | DECEMBER |  |  | 
 |  | 48 | 49 | 50 | 51 | 52 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52
 | Mission Definition Review (MDR) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Check legacy missions' info |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Test BIRDS APRS legacy boards |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Programming MCU |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Preliminary Design Review (PDR) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | EM board development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | EM components procurement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | EM board testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Integration with other subsystems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Critical Design Review (CDR) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | EM Board space environment testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | FM Board development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | FM Integration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |