## Slide 1: APRS Reference Board (APRS-R)

## Slide 2: Function and Performance
Purpose : Provide satellite APRS digipeating for Amateur Radio Community.
Function 1: Digipeater APRS packets from amateur radio stations on the ground.​
Performance 1a: Transmit satellite APRS beacon to ground​
Performance 1b: Receive and retransmit APRS packets from amateur radio stations.
Performance 1c: Transfer the received data packets to desired micro controller.

## Slide 3: Function and Performace
Function 2 : Store the received data.​
Performance 2a: Store the data to satellite’s specified memory location.​
Function 3 : Send data to the main ground stations​.
Performance 3a: Transfer stored data to COMM MCU for download via UHF 4800 bps to ground stations.

## Slide 4: PBS
Satellite
1.1
Payload
1.1.2
APRS Reference
1.1.2.1
Transceiver
1.1.2.1.1
Terminal Node Controller (TNC)
1.1.2.1.2
Main Control Unit (MCU)
1.1.2.1.3
Memory
1.1.2.1.4
VHF Antenna
1.1.2.1.5

## Slide 5: WBS
Payload
1.1.2
APRS Reference
1.1.2.1
Transceiver
1.1.2.1.1
Terminal Node Controller (TNC)
1.1.2.1.2
Procurement
1.1.2.1.1.1
Assemble
1.1.2.1.1.2
Test
1.1.2.1.1.3
Procurement
1.1.2.1.2.1
Assemble
1.1.2.1.2.2
Test
1.1.2.1.2.3

## Slide 6: WBS (cont’l)
Payload
1.1.2
APRS Reference
1.1.2.1
Main Control Unit (MCU)
1.1.2.1.3
Memory
1.1.2.1.4
Procurement
1.1.2.1.3.1
Assemble
1.1.2.1.3.2
Test
1.1.2.1.3.3
Procurement
1.1.2.1.4.1
Assemble
1.1.2.1.4.2
Test
1.1.2.1.4.3

## Slide 7: WBS (cont’l)
Payload
1.1.2
APRS Reference
1.1.2.1
Main Control Unit (MCU)
1.1.2.1.3
Memory
1.1.2.1.4
Procurement
1.1.2.1.3.1
Assemble
1.1.2.1.3.2
Test
1.1.2.1.3.3
Procurement
1.1.2.1.4.1
Assemble
1.1.2.1.4.2
Test
1.1.2.1.4.3

## Slide 8: WBS (cont’l)
Payload
1.1.2
APRS Reference
1.1.2.1
VHF Antenna
1.1.2.1.5
Procurement
1.1.2.1.3.1
Assemble
1.1.2.1.3.2
Test
1.1.2.1.3.3

## Slide 9: Block Diagram
9
VHF FM Transceiver
APRS Reference Payload
Flash Memory
COMM MCU
COMM TRX
Ground station
VHF band
Mission Boss
TNC/APRS module
ARPS Reference MCU
UHF band
Amateur Radio Users or
Ground Terminal
UART
1200bps
AFSK
SPI
OBC

## Slide 10: Link Budget
ELEVATION |  | 10° | 20° | 30° | 40° | 50° | 60° | 70° | 80°
GROUND STATION |  |  |  |  |  |  |  |  | 
Transmit Output Power | [W] | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
Transmit Output Power | [dBm] | 47 | 47 | 47 | 47 | 47 | 47 | 47 | 47
Antenna Gain | [dB] | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
Transmission Line Loss | [dB] | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5
EIRP | [dBm] | 59.5 | 59.5 | 59.5 | 59.5 | 59.5 | 59.5 | 59.5 | 59.5
UPLINK PATH |  |  |  |  |  |  |  |  | 
GS Antenna Pointing Loss | [dB] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Polarization Loss | [dB] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Atmospheric + Ionospheric Losses | [dB] | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4
Path Loss | [dB] | 139.2 | 135.9 | 133.5 | 130.9 | 130.3 | 129.4 | 128.7 | 128.3
Antenna Pointing Loss | [dB] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Effective Attenuation | [dB] | 137.1 | 133.8 | 131.4 | 128.8 | 128.2 | 127.3 | 126.6 | 126.2
Power at the satellite | [dBm] | -90.1 | -86.8 | -84.4 | -81.8 | -81.2 | -80.3 | -79.6 | -79.2
SATELLITE |  |  |  |  |  |  |  |  | 
Antenna Gain + Cable Loss | [dB] | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
Transceiver Received Power | [dBm] | -89.7 | -86.4 | -84 | -81.4 | -80.8 | -79.9 | -79.2 | -78.8
Minimum Received Power | [dBm] | -85 | -85 | -85 | -85 | -85 | -85 | -85 | -85
Link Margin | [dB] | -4.7 | -1.4 | 1 | 3.6 | 4.2 | 5.1 | 5.8 | 6.2

## Slide 11: Link Budget
ELEVATION |  | 10° | 20° | 30° | 40° | 50° | 60° | 70° | 80°
SATELLITE |  |  |  |  |  |  |  |  | 
Transmit Output Power | [W] | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
Transmit Output Power | [dBm] | 27.8 | 27.8 | 27.8 | 27.8 | 27.8 | 27.8 | 27.8 | 27.8
Antenna Gain + Cable Loss | [dB] | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
EIRP | [dBm] | 28.2 | 28.2 | 28.2 | 28.2 | 28.2 | 28.2 | 28.2 | 28.2
DOWNLINK PATH |  |  |  |  |  |  |  |  | 
Satellite Antenna Pointing Loss | [dB] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Polarization Loss | [dB] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Atmospheric + Ionospheric Losses | [dB] | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4
Path Loss | [dB] | 139.2 | 135.9 | 133.5 | 130.9 | 130.3 | 129.4 | 128.7 | 128.3
Antenna Pointing Loss | [dB] | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Effective Attenuation | [dB] | 149.2 | 145.9 | 143.5 | 140.9 | 140.3 | 139.4 | 138.7 | 138.3
Power at the ground station | [dBm] | -121.4 | -118.1 | -115.7 | -113.1 | -112.5 | -111.6 | -110.9 | -110.5
GROUND STATION |  |  |  |  |  |  |  |  | 
Antenna Gain | [dB] | 16 | 16 | 16 | 16 | 16 | 16 | 16 | 16
Transmission Line Loss | [dB] | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5
Transceiver Received Power | [dBm] | -108.9 | -105.6 | -103.2 | -100.6 | -100 | -99.1 | -98.4 | -98
Minimum Received Power | [dBm] | -110 | -110 | -110 | -110 | -110 | -110 | -110 | -110
Link Margin | [dB] | 1.1 | 4.4 | 6.8 | 9.4 | 10 | 10.9 | 11.6 | 12

## Slide 12: RAS
SR 1.1 – payload shall be controllable through an uplink command from a control ground station. |  | 
Design Requirements | Verification Requirements | Verification Method
Command will be sent from ground station using UHF uplink frequency | Measure receivable signal power of COMM transceiver | Using spectrum analyzer
OBC will relay the command to Mission Boss to activate APRS Reference payload | Check if the APRS/SF-WARD payload is activated/deactivated | Using terminal software to read APRS Reference MCU

## Slide 13: RAS
SR 1.2 – VHF transceiver operating in half-duplex will receive mission data from ground sensors.
SR 1.2 – VHF transceiver operating in half-duplex will receive data from amateur radio users/ground terminal. |  | 
Design Requirements | Verification Requirements | Verification Method
Receiver will demodulate FM signal received | Check AFSK output of Receiver | Using spectrum analyzer
TNC will decode received AFSK signal | Check data output of TNC | Display Serial Output of TNC through Serial Monitor on PC
APRS Reference payload will receive transmitted data and store it. | Check received data if it matches transmitted data through wired testing | Display received OBC data through Serial on PC
 | Check stored data in flash memory. | Read Flash Memory through APRS Reference Serial Interface

## Slide 14: RAS
SR 1.2 – VHF transceiver operating in half-duplex will receive mission data from ground sensors.
SR 1.3 – Payload shall store received packets (APRS message and ground sensor) into memory |  | 
Design Requirements | Verification Requirements | Verification Method
APRS Reference MCU shall process received AX.25 frame into correct fields | Check processed data of APRS Reference MCU | Display processed data through serial interface
Flash memory capacity of at least 32MB | Check specification and writable memory | Through write operations

## Slide 15: RAS
SR 1.2 – VHF transceiver operating in half-duplex will receive mission data from ground sensors.
SR 1.4 – Payload shall transmit stored data to ground station upon command from ground station using COM data downlink frequency |  | 
Design Requirements | Verification Requirements | Verification Method
COMM MCU shall read stored memory in APRS Reference Flash memory for downlink | Check data transmitted by COMM | Display received data

## Slide 16: Schedule
TASK | 2022 |  |  |  | 2023 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2024 |  |  |  |  |  |  | 
 | Dec |  |  |  | Jan |  |  |  | Feb |  |  |  | Mar |  |  |  | Apr |  |  |  | May |  |  |  | Jun |  |  |  | Jul |  |  |  | Aug |  |  |  | Sep |  |  |  | Oct |  |  |  | Nov |  |  |  | Dec |  |  |  | Jan |  |  |  | Feb |  |  | 
 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
Check legacy missions' info |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Procurement Components |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bread board model |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Programming MCU |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EM development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Integration with other satellite subsystems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Space Environment Test |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FM development and final space environment tests |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |